## Slide 1: Spectre and Meltdown: Recent Security Flaws Adam Belay, Srini Devadas, and Joel Emer

## Slide 2: Context
Performance and Security
Isolation and Integrity

## Slide 3: Attack Schema
Attacker
Domain of Victim
Secret
Channel
Transmitter
Access
Secret
Receiver
Create a channel
Create the transmitter
Launch the transmitter
Access the secret

## Slide 4: Control Speculation
I: Compute
I+1: Compute
I+2: Compute
I+3: Compute
I: Control Flow
J: Compute
J+1: Compute
J+2: Compute
K: Compute
K+1: Compute
K+2: Compute
Correct direction
Mis-speculated direction
Sequential
Instruction
Execution
Non-Sequential Instruction
Execution
Transmitter Code
Instruction to launch transmitter

## Slide 5: Building a Transmitter
Domain of Victim
Transmitter
Secret
Receiver
Channel
Access
Secret
Attacker
Pre-existing (RSA example)
Written by attacker (Meltdown)
Synthesized out of existing victim code by attacker (Spectre style)

## Slide 6: Meltdown and Spectre Attack Examples

## Slide 7: Attack: Mis-speculation exfiltrates secrets through cache
Transmitter
Cache
Receiver
Covert Channel
Side Channel
Secret
Speculative
Execution
Normal
Execution

## Slide 8: Meltdown
Problem: Attacker can influence speculative control flow
Bug: Speculative execution not subject to page permission checks
Attack: User code can read kernel data (secret)
Three steps:
Setup: flush the cache
Transmit: force speculation that depends on secret
Receive: measure cache timings

## Slide 9: Meltdown example
Setup:
clflush(timing_ptr[guess]);
Transmit:
timing_ptr[*kernel_addr];
Receive:
mfence();
s = rdtsc(); *timing_ptr[guess];
e = rdtscp();
if (e - s < CACHE_MISS_THRESHOLD)
printf(“guess was right!\n”);
Page Fault
May still read
*kernel_addr (speculatively)

## Slide 10: Spectre
Problem: Attacker can influence speculative control flow (same as before)
Attack: Exfiltrate secrets within a process address space (e.g. a web browser). Can also be used to attack the kernel.
Could use attacker provided code (JIT) or could co-opt existing program code
Same three steps! Different setup and transmitters.

## Slide 11: Spectre examples
Transmit - Bounds Check Bypass:
if (x < array1_size)
array2[array1[x] * 256];
Notes: Transmit - Bounds Check Bypass:
1: if (x < array1_size)
2: array2[array1[x] * 256];
This one is relatively simple.
The attacker trains the branch predictor to mis-predict on the branch generated by 1, at an opportune time, when x >= array1_size.
This would cause 2 to have unsafe behavior:
x in array1[x] would be out of bounds, array1[x] would evaluate to some value in m̶e̶m̶o̶r̶y̶ the cache that shouldn't be accessible through array1.
Now, all that remains is transmitting is value to an observant attacker.
Speculatively executing array2[array1[x]] would generate a prefetch, which the attacker could observe via a well-established cache observation technique like flush+reload or prime&probe. The set touched by this prefetch would leak bits [~18:6] of the normally-inaccessible value referenced by array1[x].
Speculatively executing array2[array1[x] * 256], as in this example, would leak bits [~12:0], since no bits of the value are used for the line offset in the cache (we're just left-shifting the value here, to move the interesting bits into the set index).
The attacker probably doesn't even have to work hard: predicting this branch as taken is entirely reasonable.

## Slide 12: Spectre examples
Transmit - Bounds Check Bypass:
if (x < array1_size)
array2[array1[x] * 256];
Transmit - Branch Target Injector:
fnptr_t foo = choose_function();
foo(bar);
Notes: Transmit - Branch Target Injector:
1: fnptr_t foo = choose_function();
2: foo(bar);
...
(this is not an entire attack; it's missing an exfiltration gadget. This code segment is the code targeted for malicious mis-prediction)
During normal operation, the data dependency foo makes sure that the function called is one the programmer allows and expects. That would be safe and correct.
However, a high-performance core won't wait for foo to be resolved. It will work with the assumption that this code probably executed previously, and probably recently, and will probably do the same thing as before. It will speculate the value of foo via an indirect branch table. and proceed with the guessed probably-foo value until foo is resolved.
Instructions are retired in order, so none of the instructions following the call will be retired until after foo is resolved. This means that no architectural state will change until foo is correctly computed by choose_function(). If the prediction was incorrect, the speculatively executed instructions will be simply thrown out and never retired.
The speculatively executed instructions _do_, however have side effects: cache prefetches being one example.
An attacker can take advantage of the limitations of the indirect branch predictor to cause a likely mis-prediction of foo to a known address, one corresponding to an exfiltration gadget (transmitter). This happens because the branch predictor deals in virtual addresses, and is partially tagged. It is easy for an attacher to orchestrate a series of repeated indirect branches designed to write a known indirect branch address into the table used by 2.
Now, the attacker has a means of (speculatively) jumping to an arbitrary virtual address in the victim's memory.
The attacher needs a gadget to exfiltrate the value of bar (the transmitter).
The details of this gadget depend on the system's calling convention (the slides give C, but not the underlying machine code). Let's say that the call foo(bar) looks like the following:
push bar
jump foo
If the attacker can find a sequence that looks like
T1: r0 <-- pop
T2: load r0
.. then the attacker can train the indirect branch predictor to speculate 2-->T2, and effectively transmit a subset of the bits of bar. (the cache set touched by the prefetch of r0 (bar) at T2) will leak bits [~18:6] of bar to an observant attacker (depending on the number of cache sets in the cache observed by the attacker).
If the attacker wants different bits of bar, the attacker needs a different gadget - something that will transform r0 before loading it. Unfortunately, the victim's address space has a LOT of executable instructions, and finding these gadgets is not hard. This is made worse by intel's variable-width encoding, and by the fact that a LOT of x86 instructions interact with the memory subsystem.